## Slide 1: Agenda
Επίπεδο Μεταφοράς
  Βασικές υπηρεσίες
  Ορολογία
Πολυπλεξία & Θύρες
Πρωτόκολλο UDP
  Δομή πακέτου
  Checksums
UDP vs. TCP

## Slide 2: Το επίπεδο μεταφοράς εκτελείτε στους …
end hosts.
routers.
switches.
Σε πολλαπλά από τα παραπάνω.
Notes: A

## Slide 3: How many of these services might we provide at the transport layer? Which?
Reliable transfers
Error detection
Flow Control
Bandwidth guarantees
Latency guarantees
Encryption
Message ordering
Link sharing fairness
4 or fewer
5
6
7
All 8
Notes: What kinds of services can we add at transport layer?

## Slide 4: Στο επίπεδο μεταφοράς, η μονάδα μετάδοσης καλείται …
Packet – Πακέτο
Chunk – Τεμάχιο
Segment – Τμήμα
Frame – Πλαίσιο

## Slide 5: UDP Segment
Application Data (Payload)
Source Port
Dest Port
Length
Checksum
32 bits
Notes: Header format

## Slide 6: Checksum Example
example: add two 16-bit integers
1 1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
1 0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
wraparound
sum
checksum
Note: when adding numbers, a carryout from the most significant bit needs to be added to the result
Notes: Kurose and Ross forgot to say anything about wrapping the carry and adding it to low order bit

## Slide 7: TCP sounds great! UDP…meh. Why do we need it?
It has good performance characteristics.
Sometimes all we need is error detection.
We still need to distinguish between sockets.
It basically just fills a gap in our layering model.